## Slide 1: How Physical Systems Can Learn By Themselves: What AI Can Do For Physics and what Physics can do for AI
Andrea J. Liu
University of Pennsylvania
Menachem Stern UPenn
Sam Dillavou UPenn
Jacob Wycoff UPenn
Jason Rocks UPenn/BU
Carl Goodrich UPenn/IST Austria
Daniel Hexner UChicago/Technion
Nidhi Pashine UChicago/MIT
Henrik Ronellenfitsch UPenn/Williams
Marc Miskin UPenn
Doug Durian UPenn
Eleni Katifori UPenn
Sid Nagel UChicago

## Slide 2: Your Brain Vasculature Is Amazing
http://campar.in.tum.de/Main/ProjectVascularNetworks
Brain is 2% of body mass but uses ~20% of O2
Brain vasculature provides desired outputs given inputs
Input signal: blood enters brain via arteries (input blood current)
Output signal: enhanced blood/O2 pressure drop at specific local region (output blood current)
vessels contract/dilate to achieve desired output current
Vasculature delivers localized enhanced blood current to different locations on demand (fMRI)
Can we design systems (at least on computer) that can do this?

## Slide 3: From Biological System to Physics Model
Network of pipes or edges (blood arteries/vessels/capillaries) that connect junctions or nodes
Brain vasculature has ~million edges
Input
Output
How to adjust resistance of each pipe to get desired output?
brain vasculature
flow network

## Slide 4: Neural Networks Can Be Trained for Desired Input/Output Relations
First step: apply inputs and calculate outputs
Learning cost function
Learning degrees of freedom: model parameters (node weights)
Second step: ski downhill (gradient descent) on with respect to learning DOF
Repeat until
Output 1 (1 for dog, 0 for cat)
Output 2 (1 for cat, 0 for dog)

## Slide 5: Skiing (Gradient Descent) in High Dimensions
Skiing: move downhill in altitude landscape by adjusting 2 position degrees of freedom (latitude and longitude)
Google Translate has ~100 million parameters; ChatGPT4 ~1 trillion
Training Google Translate required skiing downhill in the learning cost function landscape by adjusting ~100 million learning degrees of freedom!

## Slide 6: Neural Networks Can Be Trained for Desired Input/Output Relations
First step: apply inputs and calculate outputs
Learning cost function
Learning degrees of freedom: model parameters node weights
Second step: ski downhill on with respect to learning DOF
Repeat in flow networks! But neural networks are not real
Real systems have to obey physics
Output 1 (1 for dog, 0 for cat)
Output 2 (1 for cat, 0 for dog)

## Slide 7: Physics Imposes An Extra Complication
Physics requires that current entering each node = current exiting each node
What goes in must come out: conservation law called Kirchhoff’s law
Minimizing power dissipated in entire network enforces Kirchhoff’s law
fluid current
in
flow network
car current
on
highway network
electrical current
in
resistor circuit

## Slide 8: Double Gradient Descent for Desired Input/Output Relations
Learning cost function:
Learning degrees of freedom: pipe resistances/edge resistances
Physical cost function: dissipated power
Physical DOF: junction pressures/voltages
1st descent: Minimize physical cost function wrt physical DOF—required by physics!
2nd descent: Use gradient descent to minimize learning cost function wrt learning DOF
Skiing in 2 coupled high-D landscapes at once!
source
target
Rocks, Pashine, Goodrich, Bischofberger, Liu, Nagel PNAS 2017

## Slide 9: Double Gradient Descent: It Works!
Learning cost function:
Learning degrees of freedom: pipe resistances/edge resistances
Physical cost function: dissipated power
Physical DOF: junction pressures/voltages
1st descent: Minimize physical cost function wrt physical DOF—required by physics!
2nd descent: Use gradient descent to minimize learning cost function wrt learning DOF
Rocks, Ronellenfitsch, Liu, Nagel, Katifori PNAS 2019

## Slide 10: Double Gradient Descent Is Great! BUT…
Learning cost function:
Learning degrees of freedom: pipe resistances/edge resistances
Physical cost function: dissipated power
Physical DOF: junction pressures/voltages
1st descent: Minimize physical cost function wrt physical DOF—required by physics!
2nd descent: Use gradient descent to minimize learning cost function wrt learning DOF
source
target
Rocks, Pashine, Goodrich, Bischofberger, Liu, Nagel PNAS 2017
global: require processor

## Slide 11: Double Gradient Descent is Successful and Efficient
Can tune to Δ=1
  with essentially 100% success
  by pruning tiny fraction of bonds
tuned target response Δ
tuned target response Δ
Rocks, Pashine, Goodrich, Bischofberger, Liu, Nagel PNAS 2017

## Slide 12: 2D Lasercut Realizations In Real Life
Rocks, Pashine, Goodrich, Bischofberger, Liu, Nagel PNAS 2017
Double gradient descent on computer yields
designs that are robust in the lab

## Slide 13: 3D-Printed Realizations In Real Life
Rocks, Pashine, Goodrich, Bischofberger, Liu, Nagel PNAS 2017
Double gradient descent on computer yields
designs that are robust in the lab

## Slide 14
Drawbacks of Global Process of Double Gradient Descent
Not scalable
  Requires precise microscopic knowledge of network geometry and all the pipe resistances to evaluate learning and physical cost functions
  Requires processor to calculate direction of gradient descent (which way is downhill?)
  requires ability to modify individual pipe resistances of network
Design by minimizing cost function is inherently global and requires processor
This is a problem for neural networks, too—growth is unsustainable
  Energy required to train neural networks is doubling every 3.4 months
  Energy required to run trained networks is likewise increasing (~Argentina/Netherlands by 2027)
  Whole rivers are used to cool data centers that run trained neural networks
  In 2022, data centers used 1-1.5% of the world’s electricity

## Slide 15
Drawbacks of Global Process of Double Gradient Descent
Not scalable
  Requires precise microscopic knowledge of network geometry and all the pipe resistances to evaluate learning and physical cost functions
  Requires processor to calculate direction of gradient descent (which way is downhill?)
  requires ability to modify individual pipe resistances of network
Design by minimizing cost function is inherently global and therefore requires processor
This is a problem for neural networks, too
Can systems learn input/output relations on their own, without a processor?
The brain can

## Slide 16: Artificial vs. Real Neural Networks
Lives on processor
Learning concentrated in processor
Fragile to damage to processor
Each ChatGPT text query ~ 200 kJ
Image generation ~10,000 kJ
Output 1 (1 for dog, 0 for cat)
Output 2 (1 for cat, 0 for dog)
Doesn’t need processor
Learning is distributed
Robust to damage
Adult human brain uses ~ 2000 kJ/day
Brain controls thought, memory, senses, motor skills, every process that regulates our bodies
Take one step closer to brain by updating learning DOF with local rules

## Slide 17: Coupled Learning: Let Physics Do the Work
apply
source
leave target free
Free
apply
source
apply desired target
response
Clamped
Purely local rule
leads to gradient descent on contrast function!
Stern, Hexner, Rocks, Liu PRX 2021
Exploit contrastive learning
Scellier/Bengio Comp Neuro 2017
Kendall et al arXiv 2020
nudging
*
Cost function = (desired response -free response)2
Contrast function = Pclamped -Pfree ≥ 0 thanks to physics!

## Slide 18: Coupled Learning Can Do Allostery
Flow networks
Mechanical networks
error
N=512
N=1024
N=512
N=1024
k-model
ℓ-model
Stern, Hexner, Rocks, Liu PRX 2021

## Slide 19: Coupled Learning Can Do Classification!
Classification of handwritten digits
  Input nodes: top 25 principal components of images
  Output node 1: larger value means 0
  Output node 2: larger value means 1
edge width = conductivity
edge width = power
Stern, Hexner, Rocks, Liu PRX 2021

## Slide 20: But Coupled Learning on the Computer Is Still Not Scalable
Learning cost function:
Learning degrees of freedom: pipe resistances/edge resistances
Physical cost function: dissipated power
Physical DOF: junction pressures/voltages
1st descent: Minimize physical cost function wrt physical DOF—required by physics!
2nd descent: Use gradient descent to minimize learning cost function wrt learning DOF
source
target
Rocks, Pashine, Goodrich, Bischofberger, Liu, Nagel PNAS 2017
Global
Require processor

## Slide 21: But Coupled Learning on the Computer Is Still Not Scalable
Learning cost function:
Learning degrees of freedom: pipe resistances/edge resistances
Physical cost function: dissipated power
Physical DOF: junction pressures/voltages
1st descent: Minimize physical cost function wrt physical DOF—required by physics!
2nd descent: Use gradient descent to minimize learning cost function wrt learning DOF
source
target
In real system physics AUTOMATICALLY minimizes the physical cost function—forward calculation is free!

## Slide 22: First Generation Processor-Free Physical Learning Networks
Digital variable resistors are readily available
But how to compare local power of resistor i in free and clamped states and update Ri by coupled learning rule without memory or processor?

## Slide 23: First Generation Processor-Free Physical Learning Networks
Digital variable resistors are readily available
But how to compare local power of resistor i in free and clamped states and update Ri by coupled learning rule without memory or processor?
Solution: Build identical twin networks:
  One runs free BCs, the other runs clamped BCs
  Corresponding resistors are on same breadboard
  Circuitry implements a modified coupled learning rule:
one twin edge:
Dillavou, Stern, Liu, Durian PRApplied (2022)

## Slide 24: First Generation Processor-Free Physical Learning Networks
Digital variable resistors are readily available
But how to compare local power of resistor i in free and clamped states and update Ri by coupled learning rule without memory or processor?
Solution: Build identical twin networks:
  One runs free BCs, the other runs clamped BCs
  Corresponding resistors are on same breadboard
  Circuitry implements a modified coupled learning rule:
Dillavou, Stern, Liu, Durian PRApplied (2022)
1st-generation prototype
9 junctions/16 self-adjusting resistors

## Slide 25: Classifying Irises
4 source junctions for measurements of 4 quantities
3 target junctions for 3 types of irises
Classification accuracy = 97%! It really works!
Dillavou, Stern, Liu, Durian PRApplied (2022)

## Slide 26: Teaching an Old Network New Tricks
Dillavou, Stern, Liu, Durian PRApplied (2022)

## Slide 27: This Is Great! BUT…
Because the network is made of resistors, it is linear and it can only learn limited range of tasks
Nonlinearity is essential for wider range of learning tasks

## Slide 28: Insight into How System Learns
Learning and physical landscapes are coupled
  Learning cost function depends on physical DOF as well as learning DOF
  Physical cost function depends on learning DOF as well as physical DOF
Physical landscape evolves during learning to encode what system has learned
Learning Hessian tells us curvatures in learning phase space
Eigenvalues of HL are curvatures, eigenvectors are corresponding directions in learning phase space
Physical Hessian tells us curvatures in physical phase space

## Slide 29: Evolution of Eigenvalues with Learning of Linear Regression
Learning Hessian
HL
Physical Hessian
HP
Highest eigenvalues increase
Lowest
eigenvalues decrease
Stern, Liu, Balasubramanian, arXiv (2023)

## Slide 30: Linear Regression
Low-conductance barriers direct flow to make target more sensitive to one source than the other
T1
T2
S1
S2
Felipe Martins, Marcelo Guzman

## Slide 31
Gen 1
Discrete, linear
Gen 2
Continuous, nonlinear
Transistor based highly scalable design
Edges have slightly nonlinear IV curves
    Resistance for different gate voltages
Second Generation Processor-Free Physical Learning Networks

## Slide 32
~100μs per training step, faster than simulation (~3ms)
exact CL rule!
Second Generation Processor-Free Physical Learning Networks

## Slide 33: Learning Nonlinear Classification
Width of edges corresponds to conductance

## Slide 34: Learning XOR

## Slide 35: Learning XOR

## Slide 36: To Scale Up, Need Robustness to Manufacturing Defects
Brains incredibly robust to damage
processors aren’t
our networks are
Dillavou, Stern, Liu, Durian, PR Applied (2022)

## Slide 37: Scaling Up
  Robustness to damage implies manufacturability
  Resistance changes are calculated in parallel by every edge
  Current energy/inference ~300 pJ
  Comparable to ~500 pJ for 32-parameter neural network on most energy-efficient chip
  Next step: printed circuit boards for networks with ~100-200 edges
  Then: microfabrication of up to 107 edges on a chip
    Time to calculate outputs given inputs ~ nsec
    Energy to calculate outputs given inputs ~10 pJ
Stay tuned!

## Slide 38: Sustainability: Power Regularization
By avoiding use of processor/memory, learning circuits consume far less power than ANNs
Can lower power consumption even further with power regularization!
linear regression
allostery
Power gain increases with task complexity

## Slide 39: Summary
Simultaneous optimization of learning and physical cost functions provides systematic way of solving inverse materials design problems: very general
Coupled learning provides systematic way of developing local rules to solve inverse materials design problems
Coupled learning is robust—it works in a real system!
New kind of condensed matter: processor-free physical learning networks
Playground for studying how local changes in learning DOF lead to collective phenomenon of learning
Massively scalable design suggests it might be able to replace neural networks in applications with
  Low power requirements
  High chance of damage

## Slide 40: Thanks to
Sid Nagel
Carl Goodrich
Jason Rocks
Nidhi Pashine
Irmgard Bischofberger
  NSF DMR Materials Theory
  DOE Biomolecular Materials
  NSF UPenn MRSEC
  Simons Foundation
Eleni Katifori
Daniel Hexner
Menachem
Stern
Sam
Dillavou
Doug Durian
Marc Miskin